## Slide 1: Silent Talk: EMG-Based Gesture-to-Speech Converter
Name: M. Priyadharshni
Roll No: 22103502
B.E. Biomedical Engineering
Rathinam Technical Campus

## Slide 2: Abstract
Silent Talk is a biomedical innovation that enables communication for speech-impaired individuals using EMG signals. Muscle activity is captured through surface electrodes and processed via microcontroller and output either through offline audio (DFPlayer) or Bluetooth-based TTS. The system translates gestures into audible speech.

## Slide 3: Problem Statement
People with speech impairments struggle to express their needs. There is a need for a low-cost, wearable solution that translates hand or muscle gestures into clear, audible speech in real time.

## Slide 4: Objective
To develop a gesture-to-speech converter using EMG signals and microcontroller-based processing, aiming to help mute and paralyzed patients communicate verbally.

## Slide 5: Block Diagram
EMG Sensor → Microcontroller → Signal Processing → DF Player / Bluetooth → Speaker / Mobile App

## Slide 6: Hardware Components
- Arduino UNO
- EMG Sensor Module
- DF Player Mini / HC-05 Bluetooth Module
- Micro SD card with .mp3
- Android Phone with App
- Speaker
- Jumper Wires and Breadboard

## Slide 7: Circuit Diagram - DFPlayer Version
(Insert DFPlayer circuit diagram image here)

## Slide 8: Circuit Diagram - Bluetooth Version
(Insert Bluetooth circuit diagram image here)

## Slide 9: Working Principle
The EMG sensor detects electrical muscle signals. These signals are interpreted by the Arduino. Based on gesture patterns, either a specific audio is played using DFPlayer or text is transmitted over Bluetooth for real-time TTS.

## Slide 10: Arduino Code (Offline DF Player)
#include <DFPlayer_Mini_Mp3.h>
void setup() {
Serial.begin(9600);
mp3_set_serial(Serial);
mp3_set_volume(20);
}
void loop() {
int emgValue = analogRead(A0);
if (emgValue > 500) mp3_play(1);
}

## Slide 11: Arduino Code (Bluetooth + TTS)
void setup() {
Serial.begin(9600);
}
void loop() {
int emg = analogRead(A0);
if (emg > 500) Serial.println("Hello");
}

## Slide 12: Android App (MIT App Inventor)
- Connects to HC-05 via Bluetooth
- Converts text received to voice using TTS
- Simple UI with connect & log area

## Slide 13: Result
The system successfully detects gestures and translates them into audible speech via either DFPlayer or Android App.

## Slide 14: Future Enhancements
- AI-based gesture classification
- Wireless wearable prototype
- Multi-language support
- Cloud-based logging

## Slide 15: Conclusion
This project provides a novel solution for voice-impaired individuals, converting EMG signals to speech. It is low-cost, portable, and customizable.

## Slide 16: THANK YOU
…